## Slide 1: Programming for GCSE Topic 7.1: Principles of Communication
Teaching London Computing
William Marsh
School of Electronic Engineering and Computer Science
Queen Mary University of London

## Slide 2: Outline
Activity 1
  Encoding and modulation
  Error correction
  Multiplexing
  Communicate in both directions
Activity 2
  Low-level communication
  Clock synchronisation
  Framing

## Slide 3: Teaching Issues

## Slide 4: Teaching Issue
GCSE material on networks and communication lack concepts
  It is also quite out of date
Principles
Real-world examples

## Slide 5: From the specification
OCR GCSE Computing. Candidates should be able to:
(a) explain the advantages of networking stand-alone computers into a local area network
(b) describe the hardware needed to connect stand-alone computers into a local area network, including hub/switches, wireless access points
(c) explain the different roles of computers in a client-server and a peer-to-peer network
(d) describe, using diagrams or otherwise, the ring, bus and star network topologies

## Slide 6: From the specification
OCR GCSE Computing. Candidates should be able to:
(e) describe the differences between a local area network and a wide area network such as the internet
(f) explain the terms IP addressing, MAC addressing, packet and protocols
(g) explain the need for security measures in networks, such as user access levels, suitable passwords and encryption techniques
(h) describe and justify network policies such as acceptable use, disaster recovery, failover, back up, archiving..

## Slide 7: Activity: Transmitting Data
Simple activity
  Exchange data
  Look at principles
Elaborate activity
  Notice problem
  New principle
What's a protocol

## Slide 8: Basic Activity
Sending station
  Application: create a message
  Code: text  binary
  Modulate: binary  noise
Receiving station
  Demodulate: noise  binary
  Decode: binary  text
  Application: enjoy message

## Slide 9: Basic Activity – Code
Space | 00000 | N | 01110
A | 00001 | O | 01111
B | 00010 | P | 10000
C | 00011 | Q | 10001
D | 00100 | R | 10010
E | 00101 | S | 10011
F | 00110 | T | 10100
G | 00111 | U | 10101
H | 01000 | V | 10110
I | 01001 | W | 10111
J | 01010 | X | 11000
K | 01011 | Y | 11001
L | 01100 | Z | 11010
M | 01101 | ? | 11011

## Slide 10: Transmitting
Message format
  Read & transmit binary left to right
E
L
P
H
01100
10000
00101
01000
Two noises to signal
E 00101
0
0
1

## Slide 11: Layout – Seating
Application
Encoder
Transmitter
Application
Decoder
Receiver

## Slide 12: Transmission in Practice
Data can be sent using 2 signals
  Two noises resembles 'frequency' modulation (FM)
Real modulation schemes very complex
  Achieve very high data rates over twisted pair
  E.g. see Wikipedia article on OFDM

## Slide 13: Elaborations
Error detect using Parity
  Add a parity bit
  Acknowledge safe receipt
Send two messages at once
  Two applications on each computer
  Share link – multiplex
Reply to a message
  Communication in both directions
  Channel is multiple access

## Slide 14: Elaboration 1: Parity
E
L
P
H
011000
100001
001010
010001
Transmitter: 5 bits  6 bits
Receiver shouts 'OK'
A 000011
1 1 0 0 0 0

## Slide 15: Parity: Roles
Transmitter adds parity bit
  All code words have an even number of '1' digits
  Parity bit at right hand side: transmitted last
Receiver's decoder counts '1'
  ACK (acknowledge) correct code word
  Delete the parity bit
Retransmission
  If no acknowledgement then RETRANSMIT the code word

## Slide 16: In Practice: Parity and ACK
Error detection VITAL
  Parity cannot detect two erros
  CRC – more complex than parity
By shouting 'ok', we have cheated
  It's a third symbol!
ACK is a separate message (a reply)
  Latency: if you have to wait for a ACK then the messages over long distances are slow

## Slide 17: Elaboration 2: Multiplex
How can we share link?
E
L
P
H
01100
10000
00101
01000

## Slide 18: Elaboration 2: Multiplex
Sending station
  Application: create a message
  Multiplex: 0 or 1
  Code: text  binary
  Modulate: binary  noise
Receiving station
  Demodulate: noise  binary
  Decode: binary  text
  De-multiplex: 0 or 1
  Application: enjoy message
Each character: now 7 bits

## Slide 19: Message Format
Application
  1 bit address of destination application
Encoder
Transmitter
  Add parity
  Transmitted left to right
1A
1A 100001
1A 1000010

## Slide 20: Layout
App1
Encoder
Transmitter
Decoder
Receiver
App2
App1
App2
Take a character from one application: add 0 or 1

## Slide 21: Multiplex in Practice
Message of multiple code words
  Message length
  Error check for whole message
Source and destination address
Len=4
Src Addr
CRC
Dest Addr

## Slide 22: Elaboration 3: Multiple Access and Reply
Shared channel
  Wi-fi
  Bus-topology (old Ethernet)
How to avoid confusion?

## Slide 23: Elaboration 3: Multiple Access
Shared channel
  Wi-fi
  Bus-topology (old Ethernet)
How to avoid confusion?
  Token exchange
  Random turn taking (wifi)

## Slide 24: Elaboration 3: Multiple Access
2 stations at either end
  Sender
  Receiver
Rules for transmitting
  Listen for silence before starting
  … transmit when you have data
  If two stations transmit at once
    LONG BLAST then STOP
  Wait a bit; try again
Note: with multiple access we could have more than two tables but more addresses needed

## Slide 25: Elaboration 3: Reply
Applications are either
  Server – answers a question
  Clients – asks a question
Place one server and one client on each table
  Client asks
  Server responds
Application protocol
  Question ends with a '?'
Note: HTTP is an application protocol to display web pages. It sends messages like 'get index.html'

## Slide 26: Layout - Seating
App1
Server
Encoder
Transmitter
Decoder
Receiver
App2
Client
App2
Server
App1
Client
Decoder
Receiver
Transmitter
Encoder

## Slide 27: In Practice: Multiple Access
Multiple access is used in
  Original Ethernet
  Wifi
Switches now avoid multiple access in Ethernet
We have ignored
  Station address: MAC address is used in Ethernet, Wifi and Bluetooth

## Slide 28: In Practice: Reply
Client / server is the basis of the Internet
  E.g. web, email
  Conservations are between applications on hosts
  Ok to browse same web site twice
  Our address (1 bit) is a combination of an IP address (for a host) and TCP 'port' (for an application)
We have assumed sender address is same as destination address
  In practice, need both

## Slide 29: Communication Principles
Summary

## Slide 30: Concepts
Signal: transmit binary
Modulate: encode the binary to transmit
Parity: detect errors
Multiplex: share a link
Protocol: agree on rules of communication