## Slide 1: Programming for GCSE Topic 7.2: Internet Components
Teaching London Computing
William Marsh
School of Electronic Engineering and Computer Science
Queen Mary University of London

## Slide 2: Aims
Explain the main ideas of the Internet
Why is it call the Internet?
How is it run? Is anyone in control?
What's the Internet architecture?
What's a router?

## Slide 3: Teaching Issue
As with other network topics
  Principles not just description
  … not overwhelming complexity

## Slide 4: The Internet

## Slide 5: Hardware of the Internet
get a.mp3

## Slide 6: Three Main Components
Hosts: computers running programs
  Client: makes requests to …
  Server: provides a service; waits for requests
    Email, Web, iTunes
Transmission lines
  Copper wire, optical fibre, or radio
Routers: specialized computers that connect multiple transmission lines

## Slide 7: Packet Switching
Split a message into chunks
Add a header to each chunk
Send packets independently
Combine received packets
get a.mp3
get
h1
a.mp3
h2
get a.mp3
get
h1
a.mp3
h2
Address of Dest., Packet Id, etc

## Slide 8: Routers in Packet Switched Network
Each router is a specialized computer that receives, stores and forwards packets.

## Slide 9: Multiplexing
Link can be shared between different data streams
  Division in time – as needed, not fixed

## Slide 10: Remarkable!
Internet could have traffic jams
  Shared communication lines
  No central co-ordination
Polite behaviour (particular in TCP) prevents traffic jams (network congestion)
  … but no delivery guarantees

## Slide 11: Networks Architecture
Lots of protocols

## Slide 12: Protocol
Agreement on how to communicate
Defines:
  format of a message
  actions when data sent & received,
E.g. TCP, IP, UDP, HTTP, SMTP, Ethernet, …

## Slide 13: One Protocol for the Internet?
Too many machines in the Internet
Too many problems to solve/implement.
  How to request/receive web pages?
  How to split and combine packets?
  How to find a route to the destination?
  How to send data over physical cables?
  …
Hard to introduce new applications

## Slide 14: Layered Architecture
Build a stack of layered protocols, each:
  solves only a few (not all) problems
  defines abstraction of the Internet
Data Link
Network
Data Link
Network
Transport
Transport

## Slide 15: Layered Architecture
Build a stack of layered protocols, each:
  solves only a few (not all) problems
  defines abstraction of the Internet
Data Link
Network
Data Link
Network
Transport
Transport
Send data over cable
Find a route
Split into packets
Request web page

## Slide 16: End Hosts vs. Routers
HTTP
TCP
IP
Ethernet
interface
HTTP
TCP
IP
Ethernet
interface
IP
IP
Ethernet
interface
Ethernet
interface
SONET
interface
SONET
interface
host
host
router
router
HTTP message
TCP segment
IP packet
IP packet
IP packet

## Slide 17: Remarkable!
No one knows how many Internet computers
Decentralised organisation
Many link standards
  Ethernet
  Wifi
  … fibre optic
Internet evolves: new applications

## Slide 18: Internet Analogy: Post
Address: town + house – IP address
  Network + host
Mail sorting – router
  Letters find their way: you do not know where the sorting offices are
Various data links
  Post by train, van, bike
Shared infrastructure
  You post a letter when you want – capacity?

## Slide 19: IP Addresses

## Slide 20: Internetworking
Internetwork
  Interconnected networks
   network address
  Host-host to packet delivery
   host address

## Slide 21: IP Address
For computers (hosts) on the Internet
  Globally unique
Consists of 4 bytes. Written as “aa.bb.cc.dd”
  Hierarchical: network + host
  Router: multiple addresses
E.g. (Real)
  www.amazon.co.uk : 87.238.85.129
  www.facebook.com : 204.15.20.80
  www.eecs.qmul.ac.uk : 138.37.95.150
  frank.eecs.qmul.ac.uk : 138.37.88.242

## Slide 22: How Are Addresses Allocated?
IANA
  manages the IP address space allocations globally
  delegates five regional Internet registries (RIRs)
IANA is managed by ICANN
  under contract to the US Department of Commerce
Regional Internet Registries
  allocate IP address blocks to local ISPs
IANA The Internet Assigned Numbers Authority
ICANN Internet Corporation for Assigned Names and Numbers

## Slide 23: Regional Internet Registries
Réseaux IP Européens Network Coordination Centre (RIPE) for Europe, the Middle East, and Central Asia

## Slide 24: Who Got the Addresses?
Class A (16 million hosts) see: http://en.wikipedia.org/wiki/List_of_assigned_/8_IPv4_address_blocks
25.0.0.0/8 UK Ministry of Defence (RSRE)
51.0.0.0/8 UK Government Department for Work and Pensions
AS3161 Queen Mary and Westfield College (SuperJANET SMDS)
161.23.0.0/16 Queen Mary and Westfield College
138.37.0.0/16 Queen Mary and Westfield College
192.135.234.0/24 Queen Mary and Westfield College
192.135.231.0/24 Queen Mary and Westfield College

## Slide 25: Configuration
DNS – an example

## Slide 26: Remarkable!
No centralised configuration
Automatic configuration
  Granny takes laptop to coffee shop
  … IP address allocated
  … connected to Internet
  … can send mail

## Slide 27: Domain Name System (DNS)
Translate URL  IP
  Yellow pages of the Internet
Decentralized management
Hierarchy of DNS servers
  Root servers
  Top-level domain (TLD) servers
  Authoritative DNS servers

## Slide 28: DNS Root Servers
13+ root servers (see http://www.root-servers.org/)
Labeled A through M
B USC-ISI Marina del Rey, CA
L ICANN Los Angeles, CA
E NASA Mt View, CA
F Internet Software C. Palo Alto, CA (and 17 other locations)
I Autonomica, Stockholm (plus 3 other locations)
K RIPE London (also Amsterdam, Frankfurt)
m WIDE Tokyo
A Verisign, Dulles, VA
C Cogent, Herndon, VA (also Los Angeles)
D U Maryland College Park, MD
G US DoD Vienna, VA
H ARL Aberdeen, MD
J Verisign, ( 11 locations)

## Slide 29: Top Level Domain (TLD) Servers
Top-level domain (TLD) servers
  Generic domains (e.g., com, org, edu)
  Country domains (e.g., uk, fr, ca, jp)
  Typically managed professionally
Nominet www.nic.uk
the Internet registry
for .uk domain names

## Slide 30: Authoritative DNS Servers
Authoritative DNS servers
  Provide public records for hosts at an organization
  For the organization’s servers (e.g., Web and mail)
  Can be maintained locally or by a service provider
START-UP register a new .com?
  Add to the .com TLD
Add a new domain to myco.com
  Add to the myco authoritative sever

## Slide 31: Summary

## Slide 32: Summary
Internet – connected networks
  Independently run
Agreed protocols
  'IP' for an Internet address
Decentralised control