## Slide 1: Programming for GCSE Topic 9.1: Logic Circuits
Teaching London Computing
William Marsh
School of Electronic Engineering and Computer Science
Queen Mary University of London

## Slide 2: Aims
Show how computers are built from logic gates
  Logic gates
  … and truth tables
  … and boolean algebra
  …
  Circuit for Adding

## Slide 3: Teaching Issue
How to provide a coherent, joined up view
  Some curricula include logic circuits but it is not related to operation of a computer
  Logic circuits  add binary numbers  computer architecture

## Slide 4: Logic Gates
And, Or, Not

## Slide 5: Logic Gates
Logic gates are electronic components
  Transistors
Gates behave like switches
  Two states
  State represented by a boolean variable
open, X = 0
closed, X = 1

## Slide 6: Basic Logic Gates
OR gate
AND gate
X
Y
X
X
Y
X
Y
Y

## Slide 7: NOT Gate
Only 1 input
X
not X
X
not X

## Slide 8: Basic Logic Gates
OR gate NOT gate
AND gate
X
Y
X
Y
X
not X

## Slide 9: Connecting Gates
Output of one gate connects to input for next
X0
X1
Y
X2

## Slide 10: Truth Tables For Circuits

## Slide 11: AND, OR
OR gate
AND gate
X
Y
X
Y
X Y X . Y
0 0 0
0 1 0
1 0 0
1 1 1
X Y X + Y
0 0 0
0 1 1
1 0 1
1 1 1
True when either X or Y true
True when both X and Y true

## Slide 12: Circuit to Truth Table
Test a circuit
X0
X1
Y
X2
X2 X1 X0 Y
0 0 0
0 0 1
0 1 0
0 1 1
1 0 0
1 0 1
1 1 0
1 1 1

## Slide 13: Circuit to Truth Table
Test a circuit
X0
X1
Y
X2
X2 X1 X0 Y
0 0 0 0
0 0 1 0
0 1 0 0
0 1 1 0
1 0 0
1 0 1
1 1 0
1 1 1

## Slide 14: Circuit to Truth Table
Test a circuit
X0
X1
Y
X2
X2 X1 X0 Y
0 0 0 0
0 0 1 0
0 1 0 0
0 1 1 0
1 0 0 0
1 0 1 1
1 1 0 1
1 1 1 1
Two circuits equivalent if (and only if) they have the same truth table

## Slide 15: Translating Circuits to Boolean Algebra

## Slide 16: Circuit to Formula
Label each point in turn
X0
X1
X2
X0 or X1
(X0 or X1) and X2
not X1
((X0 or X1) and X2) or not X1

## Slide 17: De-Morgan’s Laws – Recap
Important law for exchanging AND with OR
( A . B ) = A + B
‘A and B’ is false when either A is false or B is false
( A + B ) = A . B
‘A or B’ is false when both A is false and B is false

## Slide 18: De-Morgan’s Law II
Same with circuits
Quiz: draw the other law as a circuit
A
B
A
B
( A + B ) = A . B

## Slide 19: De-Morgan’s Law III
Second law as a circuits
A
B
A
B
( A . B ) = A + B

## Slide 20: Summary
Logic circuits
  Build a computer
Truth table
  Specify a circuit
Boolean expression (formula)
  Algebraic rules
All express same thing
  Translate from one to other