## Slide 1: Programming for GCSE Topic 9.2: Circuits for Adding
Teaching London Computing
William Marsh
School of Electronic Engineering and Computer Science
Queen Mary University of London

## Slide 2: Aims
Show how computers are built from logic gates
Circuit for Adding
  … two inputs
  … three inputs – one column
  … many columns
Key Idea:
Represent numbers as binary digits
Digits as logic levels

## Slide 3: Half Adder

## Slide 4: Half Adder
Simplest circuit for binary addition
  input: two bits A and B
  output: sum S and carry C
Sums  ?  circuit
0 + 0 = 0
0 + 1 = 1
1 + 0 = 1
1 + 1 = 0 carry 1
A
B
S
C
Half-+
0
1
?
?
Half-+
Example:
Notes: 4

## Slide 5: Half Adder – Truth Table
Binary addition – truth table
  input: two bits A and B
  output: sum S and carry C
Quiz: Determine the formula for S and C
0 0 0 0
0 1 0 1
1 0 0 1
1 1 1 0
A B C S
Notes: 5
Bit of time for this (if available)‏

## Slide 6: Half Adder – Formula
Simplest circuit for binary addition
  input: two bits A and B
  output: sum S and carry C
0 0 0 0
0 1 0 1
1 0 0 1
1 1 1 0
A B C S
Quiz: draw the circuit
Notes: 6

## Slide 7: Half Adder – Circuit
Simplest circuit for binary addition
  input: two bits A and B
  output: sum S and carry C
0 0 0 0
0 1 0 1
1 0 0 1
1 1 1 0
A B C S
A
B
S
C
Notes: 7

## Slide 8: Full Adder
One Columns of a Binary Addition

## Slide 9: Full Adder – One Column
Each digit (column) of binary add has 3 inputs
  A, B and carry Cin
0 0 0 0 0
0 0 1 0 1
0 1 0 0 1
0 1 1 1 0
1 0 0 0 1
1 0 1 1 0
1 1 0 1 0
1 1 1 1 1
A B Cin Cout S
A
Full-+
Cin
B
S
Cout
A
B
S
Cout
Cin
Notes: 9

## Slide 10: Full-Adder from 2 Half Adders
Step 1: add A + B
Step 2: add carry to result
Step 3: carry
A
B
S’
C’
Half-+
S
Half-+
Cin
Cout
C’’
Notes: 10
Explain the OR gate.
Could use algebra. Step 1, equations
S’ = A!B + !AB
C’ = A + B
Cout = (S’ + C’) + Cin
S = (S’+C’)!Cin + !(S’+C’)Cin
Step 2:
Cout = A!B + !AB + Cin
Note that S’+C’ = A + B
S = (A + B)!Cin + !(A + B)Cin
= A!Cin + B!Cin + !A!BCin

## Slide 11: Ripple Adder
Add each bit, carry from previous bit
A
Full-+
Cin
B
S
Cout
Notes: 11

## Slide 12: Ripple Adder
Add each bit, carry from previous bit
A0
Full-+
Cin = 0
B0
S0
Full-+
Full-+
Cout
S1
S2
A1
B1
A2
B2
Notes: 12

## Slide 13: Syllabus

## Slide 14: Syllabus – Binary
GCSE (OCR)
  Logic circuits: and, or , not
  Truth tables
  Writing boolean expressions
AS/A2 (AQA)
  (AS) More boolean algebra
  (AS) More gates
Joined up view?
How to make sense of logic unless used e.g. adder circuit.
binary  truth table
 circuit

## Slide 15: Summary
Show how logic circuits build a computer
  Binary digits become logic inputs
  Circuits operate on numbers
Adder stages
  One column, no carry
  One column, with carry
  Many columns