## Slide 1: A Level Computer Science Topic 5: Computer Architecture and Assembly
Teaching London Computing
William Marsh
School of Electronic Engineering and Computer Science
Queen Mary University of London

## Slide 2: Aims
Understand CPU structure in more detail
  Fetch-execute cycle
  Faster CPUs
Write simple assembly code
  Use Little Man Computer
Understand principles of compiling
Compare compilers and interpreters

## Slide 3: CPU Structure
What’s in a CPU

## Slide 4: Simple Computer
Processor
  CPU
Memory
  Data
  Program instructions
I/O
  Keyboard
  Display
  Disk
Memory
Keyboard I/F
CPU
Disk
I/F
Display
I/F
data
data
addresses

## Slide 5: Memory
Each location
  has an address
  hold a value
Two interfaces
  address – which location?
  data – what value?
address
data

## Slide 6: Registers (or Accumulators)
A storage area inside the CPU
VERY FAST
Used for arguments and results to one calculation step
Control lines
Register – 1 memory location
data
Read register
Write to register

## Slide 7: CPU Structure
Accumulators
  Data for calculation
Data
  Word to/from memory
PC
  Address of next instruction
Instruction
Address
  For memory access
Program
Counter
Address
Instruction
Data
ALU
Accumulators
Control
Unit
memory
address
data
Control Unit
ALU

## Slide 8: Instructions
Instruction
  What to do: Opcode
  Where: memory address
Instructions for arithmetic
  Add, Multiply, Subtract
Memory instructions
  LOAD value from memory
  STORE value in memory
OpCode
Address

## Slide 9: Add Instruction
One address and accumulator (ACC)
  Value at address added to accumulator
ACC = ACC + Memory[Address]
Add
Address

## Slide 10: Little Man Computer
A Simulator for a Simple CPU

## Slide 11: Advantages of LMC
Very simple
Number of implementations
  Java applet
  Excel
  Flash, .net
  MacOS
Some incompatibilities
Feature: uses decimal not binary

## Slide 12: LMC CPU Structure
Visible registers shown in red
Program
Counter
Mem
Address
Instruction
MEM Data
ALU
Accumulator
Control
Unit
memory
address
data
Control Unit
ALU

## Slide 13
Memory locations
Accumulator
Program counter

## Slide 14: Windows .net LMC
Excel LMC
Flash LMC

## Slide 15: Feature Comparison
Step and Animation
  Most allow single stepping – see fetch-execute
  Animation – e.g. flash version
Can program using mnemonics
  LDA, STA, ADD …
  Supported in e.g. applet
  Not supported in Excel, Flash versions
Programming versus demonstration

## Slide 16: LMC Instructions

## Slide 17: Instructions
Opcode: 1 decimal digit
Address: two decimal digits – xx
OpCode
Address
Code | Mnemonic | Description
000 | HLT | Halt
1xx | ADD | Add: acc + memory  acc
2xx | SUB | Subtract: acc – memory  acc
3xx | STA | Store: acc  memory
5xx | LDA | Load: memory  acc
6xx | BR | Branch always
7xx | BRZ | Branch is acc zero
8xx | BRP | Branch if acc > 0
901 | IN | Input
902 | OUT | Output

## Slide 18: Add and Subtract Instruction
One address and accumulator (ACC)
  Value at address combined with accumulator value
  Accumulator changed
Add: ACC  ACC + Memory[Address]
Subtract: ACC  ACC – Memory[Address]
ADD
Address
SUB
Address

## Slide 19: Load and Store Instruction
Move data between memory and accumulator (ACC)
Load: ACC  Memory[Address]
Store: Memory[Address]  ACC
LDA
Address
STA
Address

## Slide 20: Branch Instructions
Changes program counter
May depend on accumulator (ACC) value
BR: PC  Address
BRZ: if ACC == 0 then PC  Address
BRP: if ACC > 0 then PC  Address
BR
Address

## Slide 21: Practical Exercises 1.1
Enter the program for example 1.1
Understand how to
  Enter
  Assemble / compile
  Run the program
See notes on available versions.

## Slide 22: LMC Example

## Slide 23: Compiling a Simple Program
Compiler translates high level program to low level
E.g. x = y + z
LDA y
ADD z
STA x
HLT
x
y
z

## Slide 24: Running the Simple Program
PC
IR
ACC
LDA
LDA y
ADD z
STA x
HLT
x
y 17
z 9
17

## Slide 25: Running the Simple Program
PC
IR
ACC
ADD
LDA y
ADD z
STA x
HLT
x
y 17
z 9
17
26

## Slide 26: Running the Simple Program
PC
IR
ACC
STA
LDA y
ADD z
STA x
HLT
x
y 17
z 9
26
26

## Slide 27: Running the Simple Program
PC
IR
ACC
HLT
LDA y
ADD z
STA x
HLT
x
y 17
z 9
26
26

## Slide 28: Practical Exercises 1.3-1.7
Try any of the challenge problems 1.3 to 1.7
1.4 onwards require the use of branch instructions
  If statements
  Loops
See notes for examples

## Slide 29: Fetch-Execute Cycle
How the Computer Processes Instructions

## Slide 30: Fetch-Execute
Each instruction cycle consists on two subcycles
Fetch cycle
  Load the next instruction (Opcode + address)
  Use Program Counter
Execute cycle
  Control unit interprets the opcode
  ... an operation to be executed on the data by the ALU
Start
Decode & execute instruction
Fetch next instruction
Halt

## Slide 31: Fetch Instruction
Program counter to address register
Read memory at address
Memory data to ‘Data’
‘Data’ to instruction register
Advance program counter
Program
Counter
Address
Instruction
Data
Accumulators
memory
address
data
Control Unit
ALU
1
2
3
4
ALU
Control
Unit

## Slide 32: Execute Instruction
Decode instruction
Address from instruction to ‘address register’
Access memory
Data from memory to ‘data register’
Add (e.g.) data and accumulator value
Update accumulator
Program
Counter
Address
Instruction
Data
Accumulators
memory
address
data
Control Unit
ALU
1
2
3
4
5
5
6
ALU
Control
Unit

## Slide 33
Address of memory access
Data to/from memory

## Slide 34: Summary of CPU Architecture
Memory contains data and program
  Program counter: address of next instruction
  Instructions represented in binary
  Each instruction has an ‘opcode’
Instructions contain addresses
  Addresses used to access data
Computer does ‘fetch-execute’
  ‘Execute’ depends on opcode
Computer can be built from < 10,000 electronic switches (transistors)

## Slide 35: Discussion
Could we act out the way a computer works?
Can you explain he key idea of the stored program computer simply?
Should we be amazed at the working of a computer?

## Slide 36: Practical Exercise 1.2
Review the fetch execute steps using LMC

## Slide 37: Compilers and Interpreters

## Slide 38: Compiler
Compiler translates high level program to low level
Compiled languages
  Statically typed
  Close to machine
  Examples: C, C++, (Java)
  Compiler for each CPU
LDA y
ADD z
STA x
HLT
x = y + z
11010101
10010111
01110100
10000000
source code
assembly code
object code

## Slide 39: Inside a Compiler
CPU
Parser: checks that the source code matches the grammar
Type checker: checks types of variables and expressions
Code generator: generates (optimised) code
Abstract syntax tree
x = y + z
source code
parser
type checker
code
generator
11010101
10010111
01110100
10000000
object code

## Slide 40: Principle of an Interpreter
One machine can emulate another
  ‘micro-coded’ CPU
  Intel CPUs and RISC inside
x = y + z
11010101
10010111
01110100
Code (C) in language L
CPU-X
Interpreter in X for L
Rep of C
CPU-L

## Slide 41: Java and .NET Language
Java is compiled to ‘byte code’
Byte code for Java ‘virtual machine’ (JVM)
  One compiler
  Libraries
  Other languages
The JVM is emulated on real computers
  ‘JIT’ compiler
x = y + z
11010101
10010111
01110100
Java code
CPU
Byte code interpreter
byte code
JVM
Java compiler

## Slide 42: How Does an Interpreter Work?
Example: LMC emulator
def fetch(memory):
global pc, mar
mar = pc
pc = pc + 1
readMem(memory)
def readMem(memory):
global mdr
mdr = memory[mar]
acc = 0
mdr = 0
mar = 0
pc = 0
memory = [504,105,306, 0,
11, 17,...]
State of the LMC: registers and memory
def execute(memory, opcode, arg):
global acc, mar, mdr, pc
if opcode == ADD:
mar = arg
readMem(memory)
acc = acc + mdr
elif opcode == SUB:
mar = arg
readMem(memory)
acc = acc – mdr
...
Update state following rules

## Slide 43: Practical Exercise 1.2
What would the benefits be for your pupils in completing an exercise such as this?

## Slide 44: Making a Faster Computer

## Slide 45: Clock
Steps in sequence are controlled by a clock
Clock frequency
  8086 – 10 MHz
  Pentium 4 – 3 GHz
  However, clock speeds no longer increasing much
Processing power depends on
  Clock speed
  Clock cycles to execute an instruction

## Slide 46: 1GHz Clock
109 cycles per second
  1 cycle every 1 ns
  Light travels 1 m in approx 3 ns
  Billion instructions per second (up to)
Each instruction takes longer
  … many instruction in process at once
Memory access is slower
  10 of ns

## Slide 47: Moore’s Law
Notes: http://www.intel.com/technology/mooreslaw/index.htm

## Slide 48: Faster Computer
Faster clocks
  smaller IC lines (90  45  32  22nm)
  shorter time to switch
More Registers; Bigger registers
  32  64 bits
Fetch-execute pipeline
  overlap the fetch and execute
Cache memory
Multiple cores

## Slide 49: Intel 86 Family
8086 – 1978
  16 bits
80386 – 1986
  32 bits
Pentium 4 – 2000
  32 bits  64 bits
Intel core i3, i5, i7
COMPATIBLE compiled program
More instruction
Longer words
More on chip
  floating point
  cache memory
Instructions in parallel
  pipeline
  superscalar
  multi-core

## Slide 50: Summary
A CPU executes Fetch-Execute
  Fetch: next instructions from memory
  Execute: data to/from memory and accumulator
  Opcode determines execute
One machine can emulator another
Program execution
  Compiler: translates
  Interpreter: parses then interprets
  Blend: Java or .NET and byte code