## Slide 1: Teaching Computing to GCSE
Session 1
Introduction
Theory: Binary Arithmetic
Practical: KS3 Python Programming Recap

## Slide 2: Course Outline
Week No. | Computing Theory (5:00 – 6:00) | Programming in Python (6:00 – 7:30)
24th April | Binary arithmetic | Python programming KS3 recap
1st May | Truth tables/logic diagrams | For loops and while loops
8th May | CPU Architecture | 1-D & 2-D arrays (lists)
15th May | The internet & protocols | Tracing and pseudocode
22nd May | Cybersecurity | Functions & parameters
5th June | Searching algorithms | Exception handling and debugging
12th June | Sorting algorithms | Testing programs
19th June | High level/low level languages | File handling & CSV files
26th June | Consolidation: Programming for GCSE with longer tasks | 
3rd July | Consolidation: Programming for GCSE with longer tasks | 

## Slide 3: Specification Content
OCR
How to add two 8 bit binary numbers and explain overflow errors which may occur
Binary shifts
AQA
Be able to add together up to three binary numbers
Be able to apply a binary shift to a binary number
Describe situations where binary shifts can be used
Edexcel
Understand how computers represent and manipulate numbers (unsigned integers, signed integers (sign and magnitude, two’s complement))
Understand how to perform binary arithmetic (add, shifts (logical and arithmetic)) and understand the concept of overflow

## Slide 4: Binary Recap
Each place in a binary number has a value. These values go up in multiples of 2.
We convert a binary number to decimal (aka denary) by adding the place values of the columns that contain a 1.
128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
0 | 0 | 0 | 1 | 0 | 1 | 0 | 0
16 + 4 = 20

## Slide 5: Binary Addition Recap
For the AQA specification you need to be able to add together up to three binary numbers.
1 | 1 | 1 | 1 | 0 | 1 |  | 
0 | 1 | 0 | 1 | 1 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0 | 1 | 1 | 0
0 | 0 | 1 | 0 | 0 | 1 | 0 | 0
1 | 1 | 0 | 1 | 1 | 0 | 0 | 0
Rules:
0+1 = 1
1+1 = 10 (write down 0, carry 1)
1+1+1 = 11 (write down 1, carry 1)
1+1+1+1 = 100 (write down 0, carry 0, carry 1)
Notes: 94
86
36
216

## Slide 6: Negative Numbers
There are two different methods of representing negative numbers in binary:
In both systems the most significant bit is known as the ‘sign bit’.
Sign and Magnitude
Two’s Complement

## Slide 7: Sign and Magnitude
Sign and magnitude is the simplest way of representing negative numbers in binary.
In sign and magnitude the sign bit doesn’t have a value, it simply tells us whether the number is positive or negative.
Sign | 64 | 32 | 16 | 8 | 4 | 2 | 1
1 | 0 | 0 | 1 | 0 | 1 | 0 | 0
= -20
0 = plus (+)
1 = minus (-)

## Slide 8: Activity 1a
Convert the following binary numbers that use sign and magnitude representation to decimal.
Sign | 64 | 32 | 16 | 8 | 4 | 2 | 1 | Decimal
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 
0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 
1 | 0 | 1 | 1 | 1 | 0 | 1 | 0 | 
0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 

## Slide 9: Activity 1a
Convert the following binary numbers that use sign and magnitude representation to decimal.
Sign | 64 | 32 | 16 | 8 | 4 | 2 | 1 | Decimal
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | -64
0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 65
1 | 0 | 1 | 1 | 1 | 0 | 1 | 0 | -58
0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 127

## Slide 10: Activity 1b
Convert the following decimal numbers to binary numbers that use sign and magnitude representation to decimal. Use paper for working out.
Decimal | Sign | 64 | 32 | 16 | 8 | 4 | 2 | 1
-73 |  |  |  |  |  |  |  | 
-91 |  |  |  |  |  |  |  | 
46 |  |  |  |  |  |  |  | 
102 |  |  |  |  |  |  |  | 

## Slide 11: Activity 1b
Convert the following decimal numbers to binary numbers that use sign and magnitude representation to decimal. Use paper for working out.
Decimal | Sign | 64 | 32 | 16 | 8 | 4 | 2 | 1
-73 | 1 | 1 | 0 | 0 | 1 | 0 | 0 | 1
-91 | 1 | 1 | 0 | 1 | 1 | 0 | 1 | 1
46 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0
102 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0

## Slide 12: The Problem with Sign and Magnitude
Sign and magnitude might be simple, however it causes problems when performing binary addition.
Two’s complement is an alternative method of representing negative binary numbers that works with binary addition.

## Slide 13: Two’s Complement
In two’s complement the sign bit is a negative number.
Just like a normal binary number, we convert it to decimal by adding the place values together.
-128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
1 | 1 | 1 | 0 | 1 | 1 | 0 | 0
-128 + 64 + 32 + 8 + 4 = -20

## Slide 14: Flipping the Bits
We can easily work out the positive equivalent of a negative two’s complement number using the ‘flipping the bits’ method.
Finally we add a minus sign, as the original number is negative.
 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
Original Number | 1 | 1 | 1 | 0 | 1 | 1 | 0 | 0
Flip the bits | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 1
Add 1 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0
= 20
= -20

## Slide 15: Activity 2a
Convert the following binary numbers that use two’s complement representation to decimal.
Sign | 64 | 32 | 16 | 8 | 4 | 2 | 1 | Decimal
1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 
0 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 
1 | 0 | 1 | 1 | 1 | 0 | 1 | 0 | 
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 

## Slide 16: Activity 2a
Convert the following binary numbers that use two’s complement representation to decimal.
Sign | 64 | 32 | 16 | 8 | 4 | 2 | 1 | Decimal
1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | -32
0 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 73
1 | 0 | 1 | 1 | 1 | 0 | 1 | 0 | -70
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | -1

## Slide 17: Activity 2b
Convert the following decimal numbers to binary numbers that use two’s complement representation to decimal. Use paper for working out.
Decimal | Sign | 64 | 32 | 16 | 8 | 4 | 2 | 1
-73 |  |  |  |  |  |  |  | 
-91 |  |  |  |  |  |  |  | 
46 |  |  |  |  |  |  |  | 
102 |  |  |  |  |  |  |  | 

## Slide 18: Activity 2b
Convert the following decimal numbers to binary numbers that use two’s complement representation to decimal. Use paper for working out.
Decimal | Sign | 64 | 32 | 16 | 8 | 4 | 2 | 1
-73 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 1
-91 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 1
46 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0
102 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0

## Slide 19: Logical Shift
128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
Logical shift can be used to easily multiply and divide number by powers of 2.
A logical left shift of 1 multiplies the number by 2.
A logical right shift of 1 divides the number by 2.
We pad out any empty places with 0s.
0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
0 | 0 | 0 | 0 | 1 | 0 | 0 | 0

## Slide 20: Activity 3
a) Perform a logical left shift of 1 on this number.
a) Perform a logical left shift of 2 on this number.
 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1 | Decimal
Original | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 
Shifted |  |  |  |  |  |  |  |  | 
 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1 | Decimal
Original | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 
Shifted |  |  |  |  |  |  |  |  | 

## Slide 21: Activity 3
a) Perform a logical left shift of 1 on this number.
a) Perform a logical left shift of 2 on this number.
 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1 | Decimal
Original | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 12
Shifted | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 24
 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1 | Decimal
Original | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 9
Shifted | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 36

## Slide 22: Activity 4
a) Perform a logical right shift of 1 on this number.
a) Perform a logical right shift of 2 on this number.
 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1 | Decimal
Original | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 
Shifted |  |  |  |  |  |  |  |  | 
 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1 | Decimal
Original | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 
Shifted |  |  |  |  |  |  |  |  | 

## Slide 23: Activity 4
a) Perform a logical right shift of 1 on this number.
a) Perform a logical right shift of 2 on this number.
 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1 | Decimal
Original | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 48
Shifted | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 24
 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1 | Decimal
Original | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 136
Shifted | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 34

## Slide 24: Shifting Signed Integers
= -112
-128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
1 | 0 | 0 | 1 | 0 | 0 | 0 | 0
Logical shift won’t work with negative numbers represented in two’s complement binary.
When we shift the number to the right we loose the sign bit, giving us the wrong result.
0 | 1 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0 | 0 | 0 | 0
= 72

## Slide 25: Arithmetic Shift
= -112
-128 | 64 | 32 | 16 | 8 | 4 | 2 | 1
1 | 0 | 0 | 1 | 0 | 0 | 0 | 0
Arithmetic shift solves the problem of shifting a negative two’s complement to the right.
With arithmetic shift, when shifting a number to the right we pad out the empty spaces with a copy of the sign bit.
When shifting to the left we still fill the empty places with 0s.
1 | 1 | 0 | 0 | 1 | 0 | 0 | 0
= -56
1 | 0 | 0 | 1 | 0 | 0 | 0 | 0
1

## Slide 26: Activity 5
a) Perform an right arithmetic shift of 1 on this two’s complement number.
a) Perform a right arithmetic shift of 2 on this two’s complement number.
 | -128 | 64 | 32 | 16 | 8 | 4 | 2 | 1 | Decimal
Original | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 
Shifted |  |  |  |  |  |  |  |  | 
 | -128 | 64 | 32 | 16 | 8 | 4 | 2 | 1 | Decimal
Original | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 
Shifted |  |  |  |  |  |  |  |  | 

## Slide 27: Activity 5
a) Perform an right arithmetic shift of 1 on this two’s complement number.
a) Perform a right arithmetic shift of 2 on this two’s complement number.
 | -128 | 64 | 32 | 16 | 8 | 4 | 2 | 1 | Decimal
Original | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | -80
Shifted | 1 | 1 | 0 | 1 | 1 | 0 | 0 | 0 | -40
 | -128 | 64 | 32 | 16 | 8 | 4 | 2 | 1 | Decimal
Original | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 24
Shifted | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 6

## Slide 28: Activity 6
a) Perform an left arithmetic shift of 1 on this two’s complement number.
a) Perform a left arithmetic shift of 2 on this two’s complement number.
 | -128 | 64 | 32 | 16 | 8 | 4 | 2 | 1 | Decimal
Original | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 
Shifted |  |  |  |  |  |  |  |  | 
 | -128 | 64 | 32 | 16 | 8 | 4 | 2 | 1 | Decimal
Original | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 
Shifted |  |  |  |  |  |  |  |  | 

## Slide 29: Activity 6
a) Perform an left arithmetic shift of 1 on this two’s complement number.
a) Perform a left arithmetic shift of 2 on this two’s complement number.
 | -128 | 64 | 32 | 16 | 8 | 4 | 2 | 1 | Decimal
Original | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 40
Shifted | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 80
 | -128 | 64 | 32 | 16 | 8 | 4 | 2 | 1 | Decimal
Original | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 27
Shifted | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 0 | 108

## Slide 30: Break
After the break we will recap Python Programming for KS3